1. GPIO
2. I2C DISPLAY
3. PONG
4. NETWORK
GPIO
references:
https://elinux.org/RPi_GPIO_Code_Samples
https://www.pieter-jan.com/node/15

according to raspberry pi 4 bcm2711 data sheet:

to set gpio pin as input/output: GPFSEL

-> to set gpio9 as output we need to set bit 27-29th of GPFSEL0 to 000
GPFSEL0 &= ~(0b111 << 27);
to set gpio9 as output bit 29 - 27th to 001
GPFSEL0 |= 0b1 << 27;

to set output on gpio pin: GPSET

to set gpio9 high:
GPSET1 |= 1<< 9

gpclr works the same

to read input on gpio pin: GPLEV
SUM UP:
#define INP_GPIO(g)   *(gpio.addr + ((g)/10)) &= ~(7<<(((g)%10)*3))
#define OUT_GPIO(g)   *(gpio.addr + ((g)/10)) |=  (1<<(((g)%10)*3))

#define GPIO_SET  *(gpio.addr + 7)  // sets   bits which are 1 ignores bits which are 0
#define GPIO_CLR  *(gpio.addr + 10) // clears bits which are 1 ignores bits which are 0

#define GPIO_READ(g)  *(gpio.addr + 13) &= (1<<(g))

//fuction which detect button is pressed, parameter gpiopin number, return true if pressed else false
bool button_pressed(int button)
{
    if(GPIO_READ(button))return false;
    return true;
}

// set buzzer as output, 5 buttons as input
void setup_gpio()
{
    INP_GPIO(BeepPin);
    OUT_GPIO(BeepPin);
    INP_GPIO(UP);
    INP_GPIO(DOWN);
    INP_GPIO(LEFT);
    INP_GPIO(RIGHT);
    INP_GPIO(ENTER);
}
I2C Display
write to i2c device
void Display::writeI2C(unsigned char* data, int bytes)
{
    int i2cHandle;
    int i2cAddress = OLED_I2C_ADDRESS;
    char deviceName[40];
    sprintf(deviceName, "/dev/i2c-1");
    if ((i2cHandle = open(deviceName, O_RDWR)) < 0)
    {
        printf("error opening I2C\n");
    }

    else
    {
        if (ioctl(i2cHandle, I2C_SLAVE, i2cAddress) < 0)
        {
            printf("Error at ioctl\n");
        }
        else
        {
            write(i2cHandle, data, bytes);
        }
    }
    close(*deviceName);
}

display command to set start line

#define WIDTH                                       128
#define HEIGHT                                      64

#define OLED_I2C_ADDRESS                            0x3C
#define OLED_SETSTARTLINE                           0x40

init display

void Display::display_init()
{
    unsigned char initSequence[26] = { 0x00, 0xAE, 0xA8, 0x3f, 0xD3, 0x00 ,0x40, 0xA1, 0xC8, 0xDA, 0x12, 0x81, 0x7F, 0xA4, 0xA6, 0xD5, 0x80, 0x8D, 0x14, 0xD9, 0x22, 0xD8, 0x30, 0x20, 0x00, 0xAF };
    writeI2C(initSequence, 26);

    unsigned char setFullRange[7] = { 0x00, 0x21, 0x00, 0x7F, 0x22, 0x00, 0x07 };
    writeI2C(setFullRange, 7);
}

pixel map

to display a full image to display we need 128 * 64/8 = 1024 bytes + 1 command byte to set startline = 1025 bytes buffer
static unsigned char img[1025];
unsigned char Display::img[1025] = {0};
img[0] = OLED_SETSTARTLINE;

to set pixel on we need to write 1 to the bit in buffer then write to display.
to find the bit of pixel(x, y)
#define nth_byte_pixel(x, y)                        ((x) +(y)/8*128 + 1)
#define nth_bit_pixel(x, y)                         ((y)%8)

void Display::draw_pixel(int x, int y, int color)
{
    if (x >= 0 && x < WIDTH && y >= 0 && y < HEIGHT)
    {
        img[nth_byte_pixel(x, y)] |= color << nth_bit_pixel(x, y);
    }
}

void Display::display(bool should_close)
{
    writeI2C(img, sizeof(img), should_close);
}
Pong

ball_position is array of 2 element that contains x and y position of the ball
p1_position for player 1
p2_position for player 2
and ball_velocity stores velocity of the ball in x and y axis

class Pong:
    def __init__(self):
        self.ball_position = [(DISPLAY_WIDTH - BALL_SIZE)/2, (DISPLAY_HEIGHT - BALL_SIZE) / 2]
        self.p1_position = [BALL_SIZE, (DISPLAY_HEIGHT - BAT_LENGTH) / 2]
        self.p2_position = [DISPLAY_WIDTH - 2 * BALL_SIZE, (DISPLAY_HEIGHT - BAT_LENGTH) / 2]
        self.ball_velocity = [random.choice((-4, 4)), 0]

with position and velocity of the ball we can always predict the movement of the ball
def calc_ball_positions(game):
x = game.ball_position[0] + BALL_SIZE / 2
    y = game.ball_position[1] + BALL_SIZE / 2
    velx = game.ball_velocity[0]
    vely = game.ball_velocity[1]

    result = [(x, y)]
    for i in range(20):
        if vely > 0:
            x += (DISPLAY_HEIGHT - BALL_SIZE / 2 - y) / vely * velx
            vely *= -1
            y = DISPLAY_HEIGHT - BALL_SIZE / 2
            result.append((x, y))
        elif vely < 0:
            x += (0 + BALL_SIZE / 2 - y) / vely * velx
            vely *= -1
            y = 0 + BALL_SIZE / 2
            result.append((x, y))
        else:
            if velx > 0:
                result.append((128, y))
                break
            else:
                result.append((0, y))
                break
        if x > 128 or x < 0:
            break
    return result

bot:
from the list of predicted positions of ball we have atleast	two point. We can draw	from these two point a linear f(x) = ax + b then we can calculate
position we have to move our bot to

def bot(game):
    if game.ball_velocity[0] > 0 and game.ball_position[0] > DISPLAY_WIDTH / 5:
        y = game.ball_position[1] + BALL_SIZE // 2
        if game.ball_velocity[1] != 0:
            positions = calc_ball_positions(game)
            a = (positions[-1][1] - positions[-2][1]) / (positions[-1][0] - positions[-2][0])
            b = positions[-1][1] - a * positions[-1][0]
            y = a * game.p2_position[0] + b + BALL_SIZE // 2

        if y <= game.p2_position[1] + BAT_LENGTH / 2:
            game.move_player(2, -PLAYER_SPEED)
        if y >= game.p2_position[1] + BAT_LENGTH / 2:
            game.move_player(2, PLAYER_SPEED)

Network
sending raw data via socket, on the raspberry pi with c++ we send char(0-255) format
on pc side with python data is being send in 'utf-8' format (0 – 127)
so for each byte of data, it need to be splitted in two bytes and add up when received

def help_get_data(self, result, item):
        if item >= 0:
            item = int(item)
        else:
            item = int(256 + item)
        result.append(chr(item//2))
        result.append(chr(item - item//2))

def get_data(self):
        result = []
        self.help_get_data(result, self.p1_position[1])
        self.help_get_data(result, self.p2_position[1])
        self.help_get_data(result, self.ball_position[0])
        self.help_get_data(result, self.ball_position[1])
        self.help_get_data(result, self.ball_velocity[0])
        self.help_get_data(result, self.ball_velocity[1])
        result = "".join(result)
        return result

data is sent in unsigned format and when we received a byte that greater than 127 we know
it must be a negative data

def help_set_data(self, x, y):
        if x + y < 200:
            return x + y
        else:
            return x + y - 256

def set_data(self, data):
        self.p1_position[1] = self.help_set_data(data[0], data[1])
        self.p2_position[1] = self.help_set_data(data[2], data[3])
        self.ball_position[0] = self.help_set_data(data[4], data[5])
        self.ball_position[1] = self.help_set_data(data[6], data[7])
        self.ball_velocity[0] = self.help_set_data(data[8], data[9])
        self.ball_velocity[1] = self.help_set_data(data[10], data[11])